## Slide 1: Bare-Metal OS for a Raspberry Pi4
Final Presentation Andrea Seehuber & Luca Fässler Operating Systems Lecture Spring Semester 2026
June 2026

## Slide 2: Outline
1. | Problem Statement / Motivation
2. | Hardware and Software Setup
3. | System Architecture
4. | Live Demo
5. | Evaluation and Limitations
6. | Lessons Learned and Conclusion

## Slide 3: Problem Statement / Motivation
Goal: Build a small OS kernel from scratch on real hardware
No Linux, no standard C runtime, no user space
Show core OS concepts in a concrete embedded system
Main challenge: combine scheduling, hardware access, I/O, and diagnostics

## Slide 4: Hardware and Software Setup
Raspberyy Pi 4, BCM2711, ARM Cortex-A72
Sense HAT with:
    8x8 RGB LED Matrix
    Joystick
    Pressure, Humidity, Temperature Sensors
UART as Control/Debug interface
HDMI as visual output
C & AArch64 assembly
Built with Makefile and AArch64 bare-metal cross compiler
Output: kernel8.img

## Slide 5: System Architecture
MMIO Layer:
- Direct access to peripheral registers
Drivers:
- UART, GPIO, I2C, timer, interrupts, HDMI framebuffer
Kernel Mechanisms:
- Task system, scheduler, mutexes, wait queues, heap, logging, tracing, diagnostics
Kernel Tasks:
- System tasks and user-controllable tasks

## Slide 6: Boot and Initialization
AArch64 assembly
C main
UART
heap & logging
I2C & HDMI
task system & scheduler
interrupts & timer
System Tasks
Shell
hdmi_console
joystick
led
Sets initial Stack
Clears .bss
Jumps into C main

## Slide 7: Task System and Cooperative Scheduler
Static task table
Each task has: ID, state, flags, stack pointer, name, private stack
Cooperative Scheduling: Tasks must yield, sleep, block or exit
Round-Robin selection of ready tasks
Idle task runs if no task is ready
Task states:
  READY, RUNNING, SLEEPING, BLOCKED, DYING
find next READY task
switch context
if none ready: run idle task

## Slide 8
Live Demo

## Slide 9: Evaluation and Limitations
Achieved:
      Custom Kernel boots on Pi4
      Cooperative scheduler works
      UART shell and joystick menu work
      HDMI output work
      Sense HAT LED and sensors integrated
      Tasks can be started/stopped interactively
      Runtime diagnostics implemented
Limitations:
      I2C still timing-sensitive
      HDMI rendering is complex and error-prone
      Cooperative scheduler depends on well-behaved tasks
      No user/kernel separation
      No virtual memory
      No filesystem
      No memory protection

## Slide 10: Lessons Learned and Conclusion
Lessons learned:
      Bare-metal development requires careful initialization order
      Hardware documentation is essential
      Debugging without OS support is slow but educational
      Cooperative scheduling is simple, but shifts responsibility to tasks
      Shared Hardware needs clear ownership
      Diagnostics are not optional; they are necessary for debugging
Conclusion:
      Built a compact embedded OS kernel
      Demnstrates real OS mechanisms on real hardware
      Good foundation for future improvements:
        better I2C recovery
        preemptive scheduling
        stronger memory/stack checks
        persistent storage/logging